## Slide 1
Hydrogen Sulfide (H2S) Safety Practices and
Methods of Detection
H2S
Notes: References:
ANSI Z390.1-2017
API 49 and 55
Texas Statewide Rule 36, Hydrogen Sulfide Safety
Instructor:
This course is designed to meet the requirements of ANSI Z390.1, including:
Hazards
Protection
Requirements of the ANSI Standard.
What the Instructor should do:
Introduce the Course
What Participant/s should do: Actively participate in the learning, including structured discussions.
Reference Material Used:
Class Props: Respiratory Protection, Personal H2S Monitors

## Slide 2: Objectives:
  Introduce safety practices related to H2S
  Discuss methos of detection for H2S
Notes: Appendix C of ANSI/ASSE Z390.1 requires you to cover the safety practices to eliminate or reduce the hazards and methods to detect and warn workers about unsafe environments.

## Slide 3
Even though H2S has very strong odor, it’s warning properties are poor.
Often times, employees think that just because they can’t smell H2S that it’s not present.
If odor is detected, leave area until source is identified, controlled, and area made safe.
General Safety

## Slide 4
Notes: When leaving area with H2S, go upwind or across wind.
Never with wind.
Go to higher elevation such as a hill.
Do not return until area is made safe.

## Slide 5: General Safety
If you don’t have proper respiratory protection, STAY OUT!
Use warning signs to alert personnel.
Use fencing to keep unauthorized personnel out.

## Slide 6: General Safety – Wind Direction Indicators
Post wind direction indicators in areas where H2S is present or has potential to be present.
Wind direction indicators give visual cue as to presence and direction of wind.

## Slide 7: General Safety
Use wind direction indicators, such as…
  Windsocks
  Flags
  Banners
  Streamers
Use H2S monitors and detectors

## Slide 8: General Safety - Signs
Signs to indicate the potential for or the presence of H2S
Signs to prohibit smoking
Signs to prohibit ignition sources
Other signs as needed
Notes: Remember, the ignition temperature of H2S is 500 degrees. A cigarette is 1400 degrees and an oxy-acetylene torch is 1200 degrees.

## Slide 9: General Safety - Fences
Fence off dangerous areas, including:
  Tanks,
  Open pits,
  Wellheads
Install fences far enough away
Post signs on fences

## Slide 10: Monitoring Equipment
Two basic types of monitoring equipment:
  Fixed
  Portable

## Slide 12: Monitoring Equipment - Fixed
Used in permanent locations
Can detect single or multiple gases
Have reset alarm level
Have audio and visual alarms

## Slide 14: Monitoring Equipment - Portable
Two basic types of portable monitoring equipment:
  Electronic
  Non-electronic

## Slide 15
Can be single gas or multi-gas
Usually handheld, clipped to belt, or carried in shirt pocket (should be in the breathing zone)
Some have LCD
Some alarm only
Portable Electronic Monitors
Notes: Portable Electronic Monitors
Can be single gas or multi-gas
Usually handheld, clipped to belt, or carried in shirt pocket (should be in the breathing zone)
Some have LCD
Some alarm only

## Slide 16: Portable Electronic
Portable Electronic
Notes: Portable Electronic
Can be single gas or multi-gas
Usually handheld, clipped to belt, or carried in shirt pocket (should be in the breathing zone)
Some have LCD
Some alarm only

## Slide 17: Portable Electronic
Diffusion type monitors have a sensor that allows gas to enter, then uses microprocessor to determine the amount of gas present

## Slide 19: Portable Electronic Monitor
‘BW Clip4’ app
Notes: The Honeywell BW Clip4 app duplicates the experience of operating a BW Clip4 handheld gas monitor. It comes with an interactive tutorial, which simulates navigation through the BW Clip4 user interface via the same buttons and display as an actual instrument. By default, the app shows normal readings for configured sensors. With the Honeywell BW Clip4 app, you can: - Familiarize yourself with the instrument and its functional features - Review key product features and specifications - Simulate sensor readings and alarm conditions - Review in-the-box and additional accessories - Provide feedback on the instrument and mobile app

## Slide 20: Portable Electronic - Advantages
Accurate
Light weight
“Go anywhere”
Easy to Use
Low Cost

## Slide 21: Portable Electronic - Disadvantages
Monitors must be calibrated and tested
Must order calibration gas
Sensors expire
Calibration gas expires
Sensors can be “overloaded”

## Slide 22: Portable Non-electronic
Pump draws known amount of air through tube filled with reagent
Reagent changes color
Amount of color determines amount of gas present
Notes: Discuss how to use pump and tubes

## Slide 23: Portable Non-electronic: Advantages
Relatively low cost
No batteries
Easy to use
Notes: Discuss how to use pump and tubes

## Slide 24: Portable Non-electronic: Disadvantages
Accuracy is about + 25%
Pumps can leak
H2S can corrode the pump
Have broken glass tubes
Notes: Discuss how to use pump and tubes

## Slide 25: Portable Non-electronic: Disadvantages
Tubes expire
Cannot mix pumps and tubes from different manufactures
Colors may be hard to read
Notes: Discuss how to use pump and tubes

## Slide 26
Hydrogen Sulfide (H2S) Safety Practices and
Methods of Detection
H2S
Notes: We discussed safety practices and methods of detection for Hydrogen Sulfide.