## Slide 1
Excavation
Notes: This slide gives the name of the course: Excavation Safety Competent Person Training Program. This slide is animated - - showing the light getting larger.

## Slide 2
The fatality rate for cave-ins is fifteen times greater than for other construction accidents.
8’
5’
Unstable wedge weighs 16,000 lbs.
Notes: The fatality rate for cave-ins is fifteen times greater than for other construction accidents.

## Slide 3
OSHA Review of Cave-In Fatalities for 2003
24%
Chart: 
| Improperly used | Available but not in use | Not available
East | 24 | 12 | 64
Protective Measures in the Fatalities
Improperly used
Available but not in use
Not available
24%
12%
64%

## Slide 4
OSHA Standard 29 CFR 1926.650-652
Subpart P
OSHA is the Occupational Safety and Health Administration, which is an agency within the Federal Department of Labor. They are charged with promulgating and enforcing workplace safety regulations, which are found in Title 29 of the Code of Federal Regulations, which is the Labor title. Part 1926 contains the regulations for the Construction Industry. Sections 650-652 contain the Excavation regulations, which are also known as Subpart P.
Scope and Application
This standard applies to all open excavations made in the earth’s surface. Excavations are defined to include trenches.

## Slide 5
Excavation
Any man-made cut cavity, trench, or depression in an earth surface, formed by earth removal.
Narrow excavation (in relation to its length): In general, the depth is greater than the width, but the width of a trench (measured at its bottom) is not greater than 15 feet.
Trench Excavation

## Slide 6
Competent Person
Means “…one who is capable of identifying existing and predictable hazards in the surroundings or working conditions which are unsanitary, hazardous, or dangerous to the employees and who has authorization to take prompt corrective measures to eliminate them.”
Targeted Competent Persons: Supervisors & Equipment Operators

## Slide 7
Training Requirements for the Competent Person
In the preamble to the Standard, OSHA says that, “…for the purposes of this standard, one must have had specific training in and be knowledgeable about soils analysis, the use of protective systems, and the requirements of the standard. One who does not have such training or knowledge cannot possibly be capable of recognizing existing and predictable hazards in excavation work or taking prompt corrective measures.”

## Slide 8
Specific Responsibilities of the Competent Person
Implement an adequate protective system for excavations 5+ feet deep.
Conduct tests for soil classification.
Understand standards and any data provided.
Determine proper protective system.
Recognize and reclassify soil after changes in conditions.

## Slide 9
Specific Responsibilities of the Competent Person (cont.)
Determine whether damage to excavation safety equipment renders it unusable.
Design of structural ramps.
Location of underground installations/utilities.
Monitor water removal equipment and operation.
Perform daily inspections.
Determine the necessity for a protective system if less than 5 feet deep.

## Slide 10
Yes
No
86%
14%
OSHA Review of
Cave-In Fatalities for 2003
Was the competent person on-site at the time of the fatality?

## Slide 11
Options of the Competent Person
1. Use the OSHA Standard for guidance with:
  Sloping
  Shoring with timber or aluminum hydraulic shoring
  Shielding
2. Use a Registered Professional Engineer to provide:
  Tabulated data
  Manufacturers tabulated data
  A site specific design*
  (*must be registered in the state where the work is being done.)

## Slide 12
Registered Professional Engineers must be used if:
The excavation is deeper than 20 feet.
An “alternate system” (such as sheet piling) that the Standard does not provide guidance for is used.
If the excavator is at “variance” with the Standard (i.e. doing less than the Standard requires).
Note: OSHA expects that the engineer will be registered in a related area such as a civil, mechanical, geotechnical, or architectural engineer.

## Slide 13
Excavation protection solutions must either come from the OSHA Standard or a Registered Professional Engineer.
It’s a
Show-Me-In-Writing
Standard

## Slide 14
Right
Or
Wrong?

## Slide 15
All four men are at exposure.

## Slide 16
Stable Rock
Type A
Type B
Type C
OSHA Soil Classification System
Natural solid mineral matter that can be excavated with vertical sides and remain intact while exposed.
STABILITY
Soil Types
Stable Rock Means

## Slide 17
“Fallout” Effect of Fractured Rock
Fracture planes
may cause rocks
to slide
into excavation…

## Slide 18
Drilling and blasting further fractures rock.
Rock sawing further fractures rock.

## Slide 19
Fence used as
“shield” system

## Slide 20
Rock fractured by blasting
will fail during excavation.

## Slide 21
Type A Soil
Cohesive soil with an unconfined compressive strength of 1.5 ton per square foot (TSF) (144kPa) or greater.
Friction
Liquid Bonding
Cementation
Chemical Bonding
Cohesion

## Slide 22
Examples of Cohesive Soils
Clay
Silty Clay
Sandy Clay
Clay Loam
Silty Clay Loam (in some cases)
Sandy Clay Loam (in some cases)
Cemented Soils Such as Caliche and Hard Pan are also Considered Type A

## Slide 23
  Cohesive soil with an unconfined compressive strength greater than .5 TSF, but less than 1.5 TSF
  Granular cohesionless soils including angular gravel
Type B Soil

## Slide 24
Type B (cont.)
Previously disturbed soils except those that would be classified as Type C soil.
Soil that meets the unconfined compressive strength or cementation requirements of Type A, but is fissured or subject to vibration.
Dry rock that is not stable.
Material that is part of a sloped, layered system where the layers dip into the excavation on a slope less steep than four horizontal to one vertical (4H:1V), but only if the material would otherwise be classified as Type B.

## Slide 25
Type C Soil
Cohesive soil with an unconfined compressive strength of .5 TSF (48kPa) or less
Granular soils including gravel, sand, and loamy sand
Submerged soil or soil from which water is freely seeping
Submerged rock that is not stable
Material in a sloped, layered system where the layers dip into the excavation on a slope of four horizontal to one vertical (4H:1V) or steeper

## Slide 26
Protective Systems
Shielding
Sloping
Shoring

## Slide 27
Sloping
Sloping Options
Sloping sides 1½ h to 1 v (340) -- as though it were Type C soil.
Use Appendix A to classify the soil and Appendix B to determine the correct slope.
OR
Have a registered professional engineer provide:
Tabulated data for sloping or
A site-specific sloping profile

## Slide 28
Safe angle
Maximum allowable slope
Actual slope
Terms Currently Used by OSHA
The term “angle of repose”
which comes from stockpiling
is no longer used by OSHA.

## Slide 29
0 = 45
o
0 = 45
o
0 = 45
o
Type B

## Slide 30
20’ max.
1
1½
All simple-slope excavations 20 feet or less in depth shall have a maximum allowable slope of 1½:1.
Simple Slope
Excavation in Type C Soil

## Slide 31
Wrong
Right
0 = 90
o
0 = 34
o
Benching is not allowed in Type C Soil.

## Slide 32
Simple Sloping

## Slide 33
Sloping and Benching

## Slide 34
Benching
Do not put people or materials on steps above working level.

## Slide 35
Shoring
Use the timber or aluminum hydraulic shoring charts from the OSHA standard
- - or - -
have a registered professional engineer provide:
    Tabulated data
    Manufacturer’s tabulated data
    Site-specific design
Shoring braces the unstable wedges so that they cannot fail.
Shoring Options

## Slide 36
Do not exceed allowable surcharge loads.
Overloading

## Slide 37
Spoil pile height, 2 ft. max -- if OSHA’s Timber charts are used.
20,000 lbs. of equipment -- if OSHA’s Timber or Hydraulic Shoring charts are used.
1
1
1
1
OSHA: Surcharge Load Limit

## Slide 38
Upright
Cleat
Cross Brace
Mud Sill
Soil
Wale
Timber Shoring

## Slide 39
Inadequate shoring constructed from 2” x 6” pine from the local lumber yard.

## Slide 40
Steel sheet piling in “tight sheeting” application.

## Slide 41
Soldier Piling

## Slide 42
Tieback System
A Tieback System is often used with Soldier Piling or Plate & Beam Systems.
Buried Pipe

## Slide 43
“Joe Pickup” Tieback System AKA, the fly swatter.
Plate & Beam System

## Slide 44
Soldier Piers

## Slide 45
Soil Nailing

## Slide 46
Slide Rail System

## Slide 47
Slide Rail & Steel Plate

## Slide 48
Aluminum Hydraulic Shoring
Vertical Shores
Waler Systems

## Slide 49
Single Shore

## Slide 50
Installation of a Vertical Shore

## Slide 51
Removing a
Vertical Shore

## Slide 52
Gauge:
750-1000 psi
Equal Pressure
Hydraulic Shoring is an Active Shoring System

## Slide 53
Soil Arching

## Slide 57
Arches transfer the load to the legs.

## Slide 58
Soil arching at work.

## Slide 59
Soil arching does not extend past the last shore.

## Slide 60
PLYWOOD
1 1/8” CDX or 3/4” Fin Form
2’ max.
4’ max.
4’ max.
OSHA = 18” max. (manufacturer = 24”)
2’ max.
Vertical spacing of vertical shore.

## Slide 62
What about Vertical Shores in Type C Soil?

## Slide 64
Equivalent Fluid Pressure
or
Equivalent Weight Effect
PCF
A
B
C
25
45
80
60

## Slide 66
Engineered Shoring Plan

## Slide 67
Waler Systems

## Slide 68
Type C Soils

## Slide 69
4-Way Manhole Brace
With Steel Plate

## Slide 70
Shield Systems

## Slide 71
Utility Installation

## Slide 72
Utility Repair

## Slide 73
Shields do not prevent cave-ins. They protect you when the cave-in occurs.
Shield Systems
Employees may remain inside the shield when it is moved forward, but they may not be in the excavation when the shield is installed, removed, or raised vertically.

## Slide 74
Employees are exposed to unsupported walls.

## Slide 75
Shields must be certified.
Do not jury-rig or “field fabricate” your own.

## Slide 76
Shield Certification

## Slide 77
** PSF rating and depths are based on short term exposure with excavation open a period of time equal to 24 hours or less.
Type B not exceeding 45 PSF per foot of depth, and Type C nor exceeding 60 PSF per foot in depth.
Beware of Limitations to Shield Use

## Slide 78
You may not exceed the rated capacity of any shield.

## Slide 79
Steel Plate
Do not use steel plates behind shields – it can cause the shield to be overloaded...

## Slide 80
...with predictable results.

## Slide 81
You cannot make any additions to, any subtractions from, or any alterations to any shield without written consent from the manufacturers or a registered professional engineer.

## Slide 82
Do not remove braces to clear pipe.
Use arched or high clearance spreaders instead.

## Slide 83
2’ to 4’
At least 1’
Adequate Sizing
Allow 2 to 4 feet past the end of the pipe, and at least 1 foot alongside it for employee work space.

## Slide 84
What if the trench is deeper than the box is tall?

## Slide 85
If the trench is deeper than the box is tall, the upper portion of
the trench wall can collapse and bury employees inside the shield.

## Slide 86
Spoil Pile
2’ min.
18” min.
H
V
Max allowable slope from table B-1
Support or shield system must be certified for the full depth of the excavation.

## Slide 87
Use end plate to prevent exposure at end of trench shield.

## Slide 88
“Stacker” assemblies consisting of two or more shields, attached per manufacturers’ specifications, may be used.

## Slide 89
Prevent lateral shift by digging the trench with a minimum gap (4” – 6”) between the shield and the trench wall and backfilling half to two-thirds the height of the shield.
No Lateral Shift

## Slide 90
Lateral shift can result in an employee being crushed against the pipe.

## Slide 91
Check the Clearance!

## Slide 92
Check the Clearance!

## Slide 93
it is certified for the full depth.
no soil is caving under or behind it.
2’ max.
A shield or support system may ride 2’ off the bottom if:

## Slide 94
Unless he’s a munchkin, the shield is too high off the bottom.

## Slide 95
Incompetent Person